## Slide 1: Colossal Avian Changes
8/13/2024
Matthew Zhang

## Slide 2: Lightweighting

## Slide 4: CF Plates
AL top/bottom plate mass: 1.71 lb
CF top/bottom plate mass: 0.95 lb
(could get more from cutouts)
Net: 0.76lb

## Slide 5: Upright
0.5 lb
0.43 lb

## Slide 6: Front Plate
1.19lb
1.33lb

## Slide 7
1.05 lb
.79 lb

## Slide 8: Chassis Net Weight savings
8.2lb -> 6.98 lb = 1.22lb saved

## Slide 9: Top Armor
AR500: 2.81lb
Ti Grade 5: 1.67lb
Note: Can we run w/out wedge when we decide to run top armor to make weight?

## Slide 10: Motor Selection

## Slide 11: Stats
 | BA2826 1030 KV (Baseline) | BA3520 970 KV | TP 3630
Diameter (mm) | 35.6 | 43.5 | 36
Length (mm) | 46 | 46 | 60
Weight (g) | 181 | 224 | 252
Continuous Power (W) | 1550 | 2000 | 900 (1800 max)

## Slide 12: Package (Baseline)

## Slide 13: Package (BA3520)
Motor shifted up:
Need to find appropriate belt c2c
Top plate interference
Screw interference
Recommendation:
- Extend chassis front-back size to make room

## Slide 14: Package (TP 3630)
Rear support clamp mount in chassis
High KV motor requires more aggressive ratio
Front face mount plate

## Slide 15: Chassis Design Changes

## Slide 16: Front dimension increase
Move front ~ 1/8” to make room for 3530 motor, batteries, etc
Maybe move front wheels up too, could improve balance/weight dist

## Slide 17: Rear dimension increase
Move rear wall + rear wheels ~1/8” rearward
Space gained for rear wiring-pass thru
Improves wheel – pulley clearance

## Slide 18: Side Dimension Increase
Move both sides by ~1/8” outwards to make room rhino ESC and other electronics

## Slide 19: Remove Rear upright structure
Get rid of this???? Sucks for serviceability, questionable structural integrity
Maybe need to do more brainstorming on a smarter idea for this

## Slide 20: Wep Motor Mounting Plate
Make this a machined part so we don’t have to deal w the spacers
Cheap alternative: glue the spacers to the plate

## Slide 21: Dado Joint
+ Better support for upright alignment
+ Improved machinability

## Slide 22: Mouse Ear Design
Allows 1/8” endmill