## Slide 1: Weapon Belt Tension Study
9/25/2024
Colossal Avian
No Name Robotics

## Slide 2: HTD5 Belt Profile
Pitch line assumed to be at mid-line of flat portion

## Slide 3: Diameters
37.06 + Tooth * 2 + Flat*2
18 + Flat*2
Flat = 0.87 <- Flat to pitch diameter
Tooth = 2.06 <- tooth height
12.7 + Flat*2
28t*5/pi
(pitch diameter calc for 28t)
42.92mm

## Slide 4: Nominal
Tooth touch-off condition on smooth pulley
Belt pitch length = 599.61mm

## Slide 5: Tooth wear: 0.1mm
Belt pitch length = 599.27mm

## Slide 6: Tooth wear: 0.2mm
Belt pitch length = 598.92mm

## Slide 7: Tooth wear: .5mm
Belt pitch length = 597.89mm

## Slide 8: Tooth wear: 1mm
Belt pitch length = 596.17mm

## Slide 9: Conclusion
Need to be adjustable up to a at least few mm to accommodate for belt wear worst-cases